## Slide 1
HANDS-ON · BEGINNER FRIENDLY · PYTHON
Raspberry Pi Electronics
A hands-on STEM course with the Freenove Ultimate Starter Kit
Build real circuits · write real code · teach it to others
223 components
128 projects
Coded on your Pi 'edith'

## Slide 2
WHY THIS COURSE
What you'll be able to do
1
Read a circuit
Understand breadboards, resistors, and the Pi's GPIO pins — and wire them safely.
2
Write Python that moves things
Blink lights, read sensors, spin motors, and show data on a screen.
3
Think like a debugger
Predict, test, and fix — the core skill behind every project.
4
Build & teach
Finish capstone projects and run the same lessons for friends, students, or coworkers.
Raspberry Pi Electronics · STEM Course
2

## Slide 3
THE HARDWARE
The kit at a glance
223
components & parts
128
guided projects
$50
approx. kit cost
5
languages (we use Python)
What's inside (a tour)
Outputs: LEDs, RGB LED, buzzers, relay
Displays: LCD1602, 7-segment, 8x8 matrix
Motion: servo, stepper, DC motor
Analog: potentiometer, photoresistor, thermistor (+ ADC)
Sensing: ultrasonic, PIR motion, DHT11, accelerometer
Input: buttons, joystick, 4x4 keypad, IR remote
Raspberry Pi Electronics · STEM Course
3

## Slide 4
YOUR WORKFLOW
You'll code right on your Pi
No separate computer setup needed — the Pi ("edith") is already headless and reachable. You write and run all the code on it from your Windows desktop.
1
Connect
ssh edith — or open the
desktop with TigerVNC
›
2
Edit
Write Python in the Pi's
Thonny editor or nano
›
3
Wire it up
Build the circuit on the
breadboard per the diagram
›
4
Run & learn
python blink.py — watch
it work, then tweak it
Tip: Thonny (built into Raspberry Pi OS) is the friendliest editor for beginners — run, stop, and see variable values with one click.
Raspberry Pi Electronics · STEM Course
4

## Slide 5
THE PLAN
A six-session roadmap
Session 1
Foundations
Safety, breadboard, GPIO, first blink
Session 2
Outputs & sound
Button, PWM, RGB, buzzer
Session 3
Reading the world
Analog sensors, light, temperature
Session 4
Sense & display
Ultrasonic, DHT11, LCD & matrix
Session 5
Things that move
Servo, stepper, DC motor
Session 6
Capstones
Combine it all into real projects
Each session: ~90 minutes · about a third teaching, two-thirds building.
Raspberry Pi Electronics · STEM Course
5

## Slide 6
PART 1
Foundations
The handful of ideas every project rests on — learn these once, reuse them forever.

## Slide 7
FOUNDATIONS
Safety & the breadboard
!
3.3V only
Pi GPIO pins are 3.3V. Never feed 5V back into a GPIO pin — it can fry the board.
!
Power off to wire
Build and change circuits with the Pi powered down. Double-check before powering on.
!
Mind resistors
LEDs need a current-limiting resistor (usually 220Ω). No resistor = dead LED.
!
No motors on GPIO
Motors draw too much current — always drive them through the included driver chips.
How a breadboard works
1. Power rails
The long red (+) and blue (–) lines run the full length and carry power.
2. Row connections
Each horizontal row of 5 holes is electrically joined — plug parts into the same row to connect them.
3. The center gap
Splits the board so a chip can straddle it with each side isolated.
Raspberry Pi Electronics · STEM Course
7

## Slide 8
FOUNDATIONS
Meet the GPIO pins
GPIO = General-Purpose Input/Output. These 40 pins are how the Pi senses and controls the physical world.
Power pins
3.3V and 5V pins supply power to components.
Ground (GND)
The shared return path — every circuit needs one.
GPIO pins
Programmable: set HIGH/LOW to output, or read a sensor as input.
BCM numbers
We name pins by their 'BCM' number (e.g. GPIO17), not their board position.
Remember: the included GPIO extension board + ribbon cable bring all these pins onto the breadboard with clear labels — much easier than counting pins.
Raspberry Pi Electronics · STEM Course
8

## Slide 9
FOUNDATIONS
Get the code & libraries
Freenove publishes every project's wiring diagram and code for free. Grab it once on the Pi:
# on the Pi (ssh edith)
sudo apt update
sudo apt install -y python3-gpiozero git
git clone --depth 1 https://github.com/Freenove/\
Freenove_Ultimate_Starter_Kit_for_Raspberry_Pi.git
Two ways to talk to pins
gpiozero
Friendly, beginner-first. LED(17).on() and you're done. We use this.
RPi.GPIO / lgpio
Lower-level, more control. Freenove's examples often use these.
Teaching move: run it first, understand it second
Let learners get a blink working before explaining every line. The early win builds momentum; the concepts land better once they've seen the payoff.
Raspberry Pi Electronics · STEM Course
9

## Slide 10
PART 2
Core Projects
One new idea per project. Each builds on the last — by the end you've touched every kind of component.

## Slide 11
PROJECT · OUTPUT
Blink: your first program
THE IDEA
Turn an LED on and off. It sounds trivial, but it teaches the loop that powers almost everything: do something, wait, repeat.
You'll learn
Digital output (HIGH/LOW), loops, and timing with sleep().
PARTS: 1 LED, 1 × 220Ω resistor, 2 jumper wires.
from gpiozero import LED
from time import sleep
led = LED(17)
while True:
led.on()
sleep(1)
led.off()
sleep(1)
Raspberry Pi Electronics · STEM Course
11

## Slide 12
PROJECT · INPUT
Button & LED
THE IDEA
Read a button and let it control the light. Now the program responds to the real world instead of just running on a timer.
You'll learn
Digital input and event handling — making the Pi react to you.
PARTS: 1 push button, 1 LED, 1 × 220Ω resistor, wires.
from gpiozero import LED, Button
from signal import pause
led = LED(17)
button = Button(18)
button.when_pressed = led.on
button.when_released = led.off
pause() # wait for events
Raspberry Pi Electronics · STEM Course
12

## Slide 13
PROJECT · ANALOG OUT
Breathing LED & RGB color
THE IDEA
A pin is normally just on or off. PWM flicks it on and off thousands of times a second so an LED can glow at any brightness — and an RGB LED can show any color.
You'll learn
PWM (pulse-width modulation) — faking 'in-between' levels to dim and mix color.
PARTS: 1 LED + 1 RGB LED, 3 × 220Ω resistors, wires.
from gpiozero import PWMLED
from time import sleep
led = PWMLED(17)
while True:
led.pulse() # smooth fade
sleep(2)
# RGB = three PWM channels mixed
Raspberry Pi Electronics · STEM Course
13

## Slide 14
PROJECT · SOUND
Make some noise
THE IDEA
An active buzzer just beeps; a passive one plays pitches you control. Great for alarms, feedback sounds, and even little tunes.
You'll learn
Active vs passive buzzers, and generating tones / simple melodies.
PARTS: Active + passive buzzer, transistor, wires.
from gpiozero import TonalBuzzer
from gpiozero.tones import Tone
from time import sleep
buzzer = TonalBuzzer(17)
for note in ['C4','E4','G4','C5']:
buzzer.play(Tone(note))
sleep(0.4)
buzzer.stop()
Raspberry Pi Electronics · STEM Course
14

## Slide 15
PROJECT · SENSING
Reading the world: analog sensors
The Pi can't read analog voltages directly — an ADC chip in the kit converts them to numbers Python can use.
Potentiometer
A knob you turn. Teaches reading a changing value 0–100%.
Photoresistor
Senses light. Build an automatic night-light.
Thermistor
Senses temperature via resistance — a little math turns it into °C.
from gpiozero import MCP3008 # ADC channel
pot = MCP3008(0)
print(round(pot.value * 100), '%') # 0–100 as you turn the knob
Raspberry Pi Electronics · STEM Course
15

## Slide 16
PROJECT · SENSING
Distance, motion & climate
~
Ultrasonic (HC-SR04)
Bounces sound off objects to measure distance in cm — like a bat or a car's parking sensor.
O
PIR motion sensor
Detects a warm body moving nearby. The heart of any motion-triggered alarm or light.
=
DHT11 climate sensor
Reads temperature and humidity together — the basis of a weather station.
# Ultrasonic distance
from gpiozero import DistanceSensor
from time import sleep
sensor = DistanceSensor(echo=24,
trigger=23)
while True:
cm = sensor.distance * 100
print(round(cm, 1), 'cm')
sleep(0.5)
Raspberry Pi Electronics · STEM Course
16

## Slide 17
PROJECT · OUTPUT
Showing information: displays
LCD1602
Two lines of 16 characters. Perfect for showing sensor readings and messages.
7-segment display
Classic glowing digits — great for counters, clocks, and scores.
8×8 LED matrix
64 dots you can light individually to draw icons, letters, and animations.
Why displays matter for teaching
A number on a screen is the moment electronics becomes useful. Pairing a sensor with a display — "read the temperature, show it on the LCD" — is the single most satisfying beginner project, and it sets up every capstone.
Raspberry Pi Electronics · STEM Course
17

## Slide 18
PROJECT · MOTION
Things that move: motors
Servo
Rotates to a precise angle (0–180°). Use it for dials, arms, and locks.
Stepper
Turns in exact steps for full, precise rotation — think clocks and positioning.
DC motor
Spins fast and continuously. Driven through an H-bridge chip for direction control.
# Sweep a servo
from gpiozero import Servo
from time import sleep
servo = Servo(17)
servo.min(); sleep(1)
servo.mid(); sleep(1)
servo.max(); sleep(1)
Power note: motors get their own power via driver chips — never straight from a GPIO pin.
Raspberry Pi Electronics · STEM Course
18

## Slide 19
PART 3
Capstone STEM Projects
Combine sensors, logic, and displays into things that feel genuinely useful — and impressive to demo.

## Slide 20
CAPSTONES
Six projects worth showing off
Smart night-light
Photoresistor + RGB LED
Light fades on automatically as the room gets dark.
Mini weather station
DHT11 + LCD1602
Live temperature & humidity on a screen.
Ultrasonic theremin
Ultrasonic + passive buzzer
Wave your hand to change the pitch — pure fun.
Reverse parking sensor
Ultrasonic + buzzer + LEDs
Beeps faster as an object gets closer.
Keypad door lock
4×4 keypad + servo + LCD
Enter the right code to 'unlock'.
Intruder alarm
PIR + buzzer + LED
Trips an alarm when motion is detected.
Raspberry Pi Electronics · STEM Course
20

## Slide 21
FOR INSTRUCTORS
How to teach this well
1
Predict, then run
Ask "what will this do?" before running code. The surprise when they're wrong is where learning sticks.
2
Pair up
Two people per Pi: one wires, one types, then swap. Talking through it doubles retention.
3
Normalize bugs
Loose wires and typos are the lesson, not a failure. Model calm, systematic debugging.
4
One concept per project
Resist piling on. Each project should add exactly one new idea over the last.
5
End on a demo
Close every session with something that visibly works. Momentum is the best motivator.
6
Keep a parts tray
Lost resistors kill momentum. A labeled tray per pair saves huge amounts of time.
Raspberry Pi Electronics · STEM Course
21

## Slide 22
KEEP GOING
Resources & next steps
Freenove tutorial & code
github.com/Freenove/Freenove_Ultimate_Starter_Kit_for_Raspberry_Pi
Full 962-page tutorial PDF
freenove.com/fnk0020
gpiozero docs (Python library)
gpiozero.readthedocs.io
Your Pi setup guide
github.com/aecheman27-gif/RaspberryPiStandalone
Start with Blink. Get one win. The other 127 projects follow from there.